## Slide 1: Chapter 5 Lyapunov Stability

## Slide 2: Outlines
    Lyapunov Stability
    Lyapunov first method
    Preliminaries
    Lyapunov second method

## Slide 3: Lyapunov Stability
External stability.
For any system which is casual and relaxed at time t0,
the relationship between input and output is
(x(0)=0)
It is external stable or BIBO（Bounded Input Bounded Output）stable.
If the input and output are bounded

## Slide 4: Lyapunov Stability
Inner stability. (u=0)
Consider system
The solution is
If the solution could satisfy
Then we call the system is inner stable or asymptotically stable

## Slide 5: Lyapunov Stability
Remarks: relationship between outer and inner stable
  For LTI system, if the system is inner stable, then the system must be outer stable (BIBO stable)
  The outer stable LTI system may not be inner stable.
    System transfer function matrix reflects only the controllable and
    observable part of the whole system. The rest part, e.g. the
    uncontrollable and unobservable subsystem can not be reflected.
  If the system is controllable and observable, then the system inner stable is equivalent to outer stable

## Slide 6: Lyapunov Stability
Lyapunov Stability studies state stability with zero input, it is more generally defined, and can be applied to linear system, nonlinear system and time-varying system.
Lyapunov first method
Lyapunov second method

## Slide 7: Lyapunov Stability
Lyapunov Stability
If there is a state , that makes the state equation
Then is called balanced state (equilibrium).
Consider without input (autonomous system)

## Slide 8: Lyapunov Stability
For linear system ，if A is nonsingular matrix, then , there is unique equilibrium state and it is original point;
If A is singular matrix, then there are multiple states of equilibrium. There is more than one state of equilibrium for nonlinear system.
Remarks:
(1) The study of stability in sense of Lyapunov is to study the stability of system balanced point stability--------whether a disturbance movement which departures from the balanced state could go back or be restricted within a limited neighborhood around the balanced state point.
(2) The disturbance movement is system free motion----movement based on only system structure property and initial state.

## Slide 9: Lyapunov Stability
Vector norm: Considering n-dimension vector, the vector norm is defined as
The geometrical meaning of vector norm is distance.
e.g.
Super-sphere in state space with the center and radius

## Slide 10: Lyapunov Stability
(1) Lyapunov stable：
xe
x0
x1
x2
is Lyapunov stable
For any positive real number, if there is always corresponding number
the initial disturbance satisfies
and the movements caused by the initial disturbance satisfies

## Slide 11: Lyapunov Stability
(2) Asymptotically stable：
Then is asymptotically Lyapunov stable
If is Lyapunov stable, and
xe
x0
x1
x2

## Slide 12: Lyapunov Stability
(3) Global asymptotically stable (asymptotically stable in a whole)：
Then is global asymptotically Lyapunov stable
For any initial state x0, if
xe
x0
x1
x2

## Slide 13: Lyapunov Stability
(4) Unstable：
Then is unstable
xe
x0
x1
x2

## Slide 14: Lyapunov Stability
xe
x0
x1
x2
is Lyapunov stable
xe
x0
x1
x2
is asymptotically Lyapunov stable
xe
x0
x1
x2
xe
x0
x1
x2
is asymptotically stable in a whole
is Unstable

## Slide 15: Lyapunov Stability
Remarks:
(1) The asymptotically stability is more significant than stability.
(2) The asymptotically stability is equivalent with the stability definition in classic automatic control domain.
(3) For LTI system, if the matrix A is nonsingular and the sole balanced state at original is asymptotically stable, then the balanced state is asymptotically stable in a whole.

## Slide 16: Lyapunov First Method
Indirect method: Discriminate the system stability based on the system
characteristic roots or eigenvalues
Theorem 1:
For LTI system
The sufficient and necessary condition of equilibrium xe being Lyapunov stable is
all the eigenvalues of matrix A have negative real part
And eigenvalue with zero real part is the single root of minimal polynomial of A

## Slide 17
Minimal polynomial
Caylay-Hamilton theorem:
For matrix , the Eigen polynomial is
Then matrix
Zero polynomials of A is not unique, the one with minimal order makes the minimal polynomial.
For matrix , there exists polynomial that satisfies , then is called zero polynomial of A

## Slide 18
The way to get the minimal polynomial
Let m(s) be greatest common divisor of all the entries of adj(sI-A), then is the minimal polynomial of A.
Remark: the minimal polynomial of A is the least common denominator of all the entries of (sI-A)-1 .

## Slide 19: Lyapunov First Method
Example：
Try to determine the stability
f(s)=s(s+1)
It is Lyapunov stable.

## Slide 20: Lyapunov First Method
Theorem 3:
The sufficient and necessary condition of LTI system being BIBO stable is
The poles of TF are located in left part of S domain.
Theorem 2:
For LTI system
The sufficient and necessary condition of equilibrium xe being
asymptotically Lyapunov stable is

## Slide 21: Lyapunov First Method
Example：
Try to determine the stability
xe=0 is asymptotically Lyapunov stable.

## Slide 22: Lyapunov First Method
Example：
Try to determine the stability
Poles s = -3，it is BIBO stable.
it is not asymptotically Lyapunov stable.
Remark： BIBO stable asymptotically stable

## Slide 23: Preliminaries
(1) Euclidean norm
1) Euclidean norm of vectors (length)
Generally

## Slide 24: Preliminaries
2) Euclidean norm of matrices
For matrix its Euclidean norm is defined as
For example

## Slide 25: Preliminaries
(2) Quadratic function and its expression of matrix
1) Quadratic function
A quadratic function consists of n variables
2) Matrix form of Quadratic function
P is a symmetric matrix

## Slide 26: Preliminaries
3) The sign of Quadratic function
For quadratic function
P is Positive Semi-definite Matrix(P≥0)
Then is Positive Semi-definite,
P is Negative definite Matrix (P<0)
c. Negative definite: if -V(x) is positive definite, then V(x) is negative definite.
d. Negative Semi-definite
a. Positive Definite :
b. Positive Semi-definite

## Slide 27: Preliminaries
Then is unfixed
e. unfixed :
Diagonal matrix D=diag{d1,…, dn} is positive definite, iff di > 0
Identity matrix I is positive definite：
Some properties of positive matrix
If A is a positive matrix, then
If A and B are positive matrices, then

## Slide 28: Preliminaries
Example:, try to figure out the sign the following functions
5)
4)
3)
2)
1)

## Slide 29: Preliminaries
Sylvester criterion: The sufficient and necessary condition of
being positive definite is
The Order Master determinant of matrix P are greater than 0, that is
，
，…，
then
is positive definite,
is a positive definite matrix
The sign of Order Master determinant of matrix P is altering , that is
，
，…，that is
then
is negative definite,
is a negative definite matrix

## Slide 30: Preliminaries
Example: try to figure out the sign the following functions

## Slide 31: Preliminaries
Example:, try to verify that the following function is positive definite.

## Slide 32: Preliminaries
Example：
determine
to make V positive definite

## Slide 33: Preliminaries
The sufficient and necessary condition of
being positive definite is
The eigenvalues of matrix P are greater than 0, that is
then
is positive definite,
is a positive definite matrix

## Slide 34: Lyapunov Second Method
  Without solving system characteristic roots.
  Construct a scalar system energy (Lyapunov) function and analyze the function and its first order differential coefficient sign to get the correlative information of system stability.
  Basic idea: if a system is asymptotical stable, the energy of system will decay with time and approach to a (certain) minimum value.

## Slide 35: Lyapunov Second Method
Theorems of Lyapunov second method
1. For any system with state equation and balanced state , if there is a scalar function satisfying
(1) (2)
then we could say the system is asymptotically stable at .
Physical meaning: system energy is always positive.
the energy decays with time.
Additionally, (3)
then we could say the system is asymptotically stable in a whole at .

## Slide 36: Lyapunov Second Method
Example: For state equation:
Try to figure out whether it is stable.
(x1=0, x2=0) is the only balanced state.
is negative definite. When
Choose a Lyapunov function

## Slide 37: Lyapunov Second Method
Theorems of Lyapunov second method
For any system with state equation and balanced state , if there is a scalar function , satisfying
(1) (2) (3)
then we could say the system is asymptotically stable at .
Physical meaning: system energy is always positive.
the energy decays with time,
the energy remain temporarily the same at certain state
but will not stop decaying.
Additionally, (4)
then we could say the system is asymptotically stable in a whole at .

## Slide 38: Lyapunov Second Method

## Slide 39: Lyapunov Second Method
Example: For state equation:
Try to figure out whether it is stable.
(x1=0, x2=0) is the only balanced state.
is negative semi-definite.
Choose a Lyapunov function
When

## Slide 40: Lyapunov Second Method
Choose another Lyapunov function
When

## Slide 41: Lyapunov Second Method
For any system with state equation and balanced state , if there is a scalar function satisfying
(1) (2)
then we could say the system is instable at in sense of Lyapunov.
, system energy keeps increasing

## Slide 42: Lyapunov Second Method
Example: For state equation:
Try to figure out whether it is stable.
(x1=0, x2=0) is the only balanced state.
Choose a Lyapunov function
Instable

## Slide 43: Lyapunov Second Method
The Lyapunov stability analysis of linear system
If the system is asymptotically stable at , according to theorem 1, make
That means Q must be positive definite.

## Slide 44: Lyapunov Second Method
Lyapunov stability theorem of linear system
for any given positive definite matrix Q,
there is a unique symmetry positive-definite matrix P which satisfies

## Slide 45: Lyapunov Second Method
Remarks:
(1) For any given positive definite matrix Q, matrix P which satisfies
equation is unique. The system is asymptotically stable when P is positive definite.
(2) If the function , then, matrix Q could be just semi-positive definite matrix. And the system is still asymptotically stable.
(3) Generally, we choose =I, so the equation is

## Slide 46: Lyapunov Second Method
Example: For state equation:
Try to figure out whether it is stable by Lyapunov equation.

## Slide 47: Lyapunov Second Method

## Slide 48: Lyapunov Second Method
Derive positive definite matrix P
%LYAP example
A=[0 1;-1 -1];
A=A’; ％transpose of A
Q=[1 0;0 1];
P=lyap(A,Q)
end
results：P =
There is MATLAB function LYAP(A,Q) that can solve the Lyapunov equation
ATP+PA=-Q
1.5000
0.5000
0.5000
1.0000

## Slide 49: Lyapunov Second Method
Example: For state equation:
Try to figure out whether it is stable by Lyapunov equation.

## Slide 50: Lyapunov Second Method
Instable

## Slide 51: Lyapunov Second Method
For comparison, consider Lyapunov first method

## Slide 52: Lyapunov Second Method